## Slide 1: Exploring HF Signals

## Slide 2
We are going to take a look and listen to some of the different signals found on the 20 meter band and how you can use the soundcard in your PC decode them.
All of digital modes presented here require an audio connection from your transceiver to your computer to receive.

## Slide 3: 20 Meter Band Plan
Frequency (Suggested) | Mode
14.000 – 14.060 mhz | CW
14.063 – 14.069 mhz | Hellschreiber
14.068 - 14.073.5 mhz | PSK31, PSK63
14.075 – 14.078 mhz | Oliva
14.076 mhz | JT65
14.079 – 14.100 mhz | RTTY
14.100 - 14.111 mhz | Packet, WinLink, Pactor
14.230 mhz | SSTV (Slow Scan TV)
14.236 – 14.239 mhz | Digital Voice

## Slide 4: CW
Oldest form of communication on the bands
Decoding programs available that use the sound card in your computer to decode the signals
CWGET, CW Skimmer are two of the free programs available.

## Slide 5: CW Get
9A7DX from Crotia calling CQ for the CW contest this past weekend

## Slide 6: PSK
Another popular digital mode
More free programs available for you to use
DigiPan, Fldigi, True TTY, MixW
Many logging programs have PSK ability built in
Help setting up is available from web sites and user groups
Sample sounds.

## Slide 8: JT65
Designed for weak signal communication
High transmit power is not needed
Extremely slow
Requires the clock on your PC to be accurate
Free software available for download
Ken Wontor is our local expert with this mode
Sounds

## Slide 9: JT65

## Slide 10: RTTY
Radio teletype
Found from 14.079 – 14.100 typically
Free software available to decode
MixW, MMTTY, True TTY
MMTY engine used by many logging programs
Help available on line and through user groups
Sounds

## Slide 12: SSTV
Slow scan TV
Free software available for you PC
RX-SSTV, MixW, MMSSTV
Found around 14.230
Transmits one pixel on a line at a time until entire picture is transmitted
Full duty cycle can be hard on finals
Sounds

## Slide 13: Olivia
Works in conditions of high atmospheric noise
Does not require high power
Can be copied when the human ear cannot hear the signal
Two most common formats are Olivia500/16 and Olivia 100/32
There are advantages to faster typing with some formats and better decoding through noise with slower narrow formats.
Can use MixW

## Slide 14: Other modes
Hellschriber
Outperforms RTTY
Works at a comfortable typing speed
Digital voice
Free software available for these also

## Slide 15: Summary
All software shown tonight is free!!!
To receive any of these signals, all you need is a cable from the audio out on your transceiver to the soundcard on your computer.
Experiment, try new things
Try other bands for the same modes
Get on the HF bands, upgrade your license and have fun